## Slide 1: NEMS_RDM

## Slide 2: NEMS Residential Demand Module
The National Energy Modeling System
Objectives
  The module generates disaggregated projections of energy demand in the residential sector from the base year through the projection horizon by housing type and fuel type, Census division, and end-use service.
  It is an analysis tool that can assess the impacts of changes in energy markets, building and equipment technologies, and regulatory initiatives that affect the residential sector.
  The module is an integral component of the NEMS system; it provides projected energy demand to the supply and conversion modules of NEMS, and contributes to the calculation of the overall energy supply and demand balance.

## Slide 3: NEMS_DMS Theoretical approach
The NEMS Residential Demand Module is an integrated dynamic modeling system based on accounting principles and a representation of residential consumer economic behavior that generates projections of residential sector energy demand, appliance stocks, and market shares.
(중략)
Logistic or ‘logit’ functions are used to estimate the market shares of competing technologies within each end-use service. Market shares are determined for both new construction equipment decisions and replacement equipment decisions. The Technology Choice Component of the module considers the relative installed capital and operating costs of each equipment type within the logit function to calculate the market shares of the technology within the service, region, and housing type.

## Slide 7: NEMS RDM
Furnaces (electric, natural gas, liquefied petroleum gas (LPG), and distillate)
Hydronic heating systems (natural gas, distillate, and kerosene)
Heat pumps (electric air-source, natural gas, and ground-source)Wood stoves
Air conditioners (central and room)
Dishwashers
Water heaters (electric, natural gas, distillate, LPG, and solar)
Cookstoves (electric, natural gas, and LPG)
Clothes washers
Clothes dryers (electric and natural gas)
Refrigerators (with top-, side-, and bottom-mounted freezers)
Freezers (upright and chest)Lighting (general service, linear fluorescent, reflector, and exterior)
Solar photovoltaic systems
Fuel cells
Wind turbines